## Slide 1: Development of a Steer-by-Wire demonstration facility
Researcher: Masase Netshituka Supervisor: Prof. Azeem Khan
Notes: Less text

## Slide 2: Project background
Steer-by-Wire(SBW) is an emerging technology based on the evolution of steering mechanisms.
The tech is based on EPAS systems.
SBW removes the mechanical link between the steering wheel and axle entirely.
Purpose of this project is to develop an interactive and educational model for demonstration.

## Slide 3: Research
Common steering systems:
  Synchronous steering
  Rack-and-Pinion
Different Power Assisted Steering (PAS) systems:
  Hydraulic power steering (HPAS)
  Electro-hydraulic power steering (EHPAS)
  Electric power steering (EPAS)
Advantages:
  Highly flexible design
  Highly efficient
  Easy to integrate
  Increased crash safety
  Highly tailored experience
Disadvantages:
  Highly complex
  Reliability concerns
  High initial implementation cost
Steer-by-Wire
Current systems
Notes: Advanced driver assistance system

## Slide 4: Model development

## Slide 5: Steering Wheel module design
Design components:
End-stop housing system
Self-centring mechanism
Custom rotary encoder
  potentiometer
2.3 : 1 gearing ratio with 12V 270rpm motor
Design objectives:
720° Steering range
Durable design
Recentring system
± 1° steering angle resolution
120 rpm wheel rotation
Notes: Mention that feedback torque was not implemented Add SW as actual image, not background

## Slide 6: Steering Actuator module design
46,42° ± 4,6° Turning range
End-to-end turn in 1s
Ackermann theory fulfilment
± 1° steering angle resolution
Small scale
Rack-and-pinion base design
60rpm motor
Grey-code rotation direction
1:3 scale of Suzuki Fronx
Design components:
Design objectives:
Notes: Bring image to the front

## Slide 7: ECU and Control
Hardware:
Arduino Uno microcontroller
4 Quadrant drivers
Use of MATLAB/SMULINK
PID based control
Software:
EOMs derived and converted into transfer functions
PID based control methodology
2 loop system:
  Steering wheel module
  Steering Actuator module
Design objectives:
Smooth steering response
< 2s delay in response
<5% transient state overshoot

## Slide 9: Results
System tracked with a damped step with 5,2s, sinusoid in1,4s delay
Steering range of 52° (11,2%)
Ackermann criteria upheld
Custom encoder system functioned, but faced precision issues
Full-range steering in 1s achieved.
Recentering system faced challenges
  Stronger springs
  Refined steering shaft thread angle
475 mm x 545 mm overall dimensions
Step response
0,25Hz sinusoid response
Notes: Put heading for graphs

## Slide 10: Recommendations
Design is a functional display and representation of the SBW system, despite the challenges faced.
Core principles of SBW and rack-and-pinion steering are evident with wireless steering communication achieved.
Conclusion
Larger spring constant
Improved shaft thread design
Recalculation of rack and tie-rods
Implementation of Feedback torque
Microcontroller with more memory

## Slide 11: THANK YOU